CAPPL:

LEGAL_DISCL (No legal notice on IDrive startup)

nicht_aktiv

VA_WELCOMELIGHT (Welcome lights menu in iDrive. Requires change in LMA module also)

aktiv

ONLINE (Enables BMW Onine in Communications iDrive screen- Works in UK? not in USA?)

aktiv

SIM (Activate SIM for internet svc - no "GSM" service message for USA)

aktiv

ONLINE_DISABLE_CONTENT Enable BMW online while driving.

(set to content_enable)

VIDEO_DENY_COB Enable video functions while driving

(set to deny_never)

VA_CORNERINGLIGHT (Cornering lights menu. Lights come at low speed turns, with turn signals and in reverse.)

aktiv

VA_SEATCLIMA_SHORTCUT (Seat heater display comes up in iDrive when heat button pushed)

aktiv

VA_SEATHEAT_SLIDER (Seat heat hi-med-low slider in iDrive)

aktiv

VA_LONGDISTANCELIGHT (Shows Highbeam assistant menu option. (must have the hardware too for it to do anything)

aktiv

VA_ADAPTIVEHEADLIGHT (Adaptive headligh menu with Comfort and Sport options. Doesn't seem to do anything with any of the settings)

aktiv

ACOUSTIK Sets alarm sound function when locking/unlocking

LMA:

WELCOME_LIGHT_Active (Welcome lights menu in iDrive. Requires light switch in auto position)

aktiv

WL_DAUER (Does this make welcome lights stay on longer ?? )

wert_02

WL_NSW (Fog lamps with Welcome lights)

soft_einschalten

FL_UND_NSW_NICHT_GLEICHZ (Allow High beam and fog lamps on at same time)

active

BI_XENON_BEI_LH (activates your Bi Xenons flash to pass feature) works on the PRE-LCI also

aktiv (* This worked for d4rkchocolate but not for NoQuarter)

KOMBI:

BC_DIGITAL_V (digital speedometer is cluster)

aktiv

SHD:

REGENSCHLIESSEN (close sunroof with auto wipers and rain. Anyone know how to test this? doesn't work for NoQuarter)

aktiv

CAS:

KOMFORTSCHLIESSUNG_FB (Close windows via key FO

aktiv

IHKA:

GEBL_ANZEIGE_AUTO (Climate fan speed display via orange light around manual speed knob)

active

HUD:

BLINKER_AUSSTATTUNG (turn signals in HUD)

aktiv

KGM (sept 2005 onwards)

BEIKLAPPEN_B_KOMFORTSCHL Comfort folding mirrors (Needs SA430)

ASP_BORDSTEIN Passenger mirror kerb function (Needs SA4)

TCU

RINGTONE Changes incoming call ringtone

(3 settings)

Correction...

FL_UND_NSW_NICHT_GLEICHZ (Allow High beam and fog lamps on at same time)

nicht_aktiv

COMFORT FOLDING MIRRORS FOR PRE 2005/6

TMBT & TMFT (The modules were installed in the driver and passenger doors untill they moved it to the KGM module in 2005/6)

BEIKLAPPEN_B_KOMFORTSCHL Comfort folding mirrors you need SA430 INTERIOR/OUTSIDE MIRROR WITH AUTO DIP if you are retrofitting folding mirrors

Activate cycling through the entertainment choices (with steering programmable button) and skip the AM band.

NEXT_SOURCE

activ

AMBANDS

nicht_activ

Result: Works

Show true speed.

BC_DIGITAL_V_KORREKTUR

nicht_activ

Result: Works.

IHKA

Show climate fan speed display via orange LED light around manual speed knob

GEBL_ANZEIGE_AUTO

activ

Result: Works

CAS:

ER_KEYOUT_AUTOVR (Unlock doors after pressing Stop Button. Driver door only or all doors selected in iDrive preferences)

aktiv

HUD:

BLINKER_AUSSTATTUNG (turn signals in HUD)

aktiv

working

VIDEO_DENY_COB Enable video functions while driving

(set to deny_never)

working

CAPPL

MDrive

activ

HUD_M

activ

HUD

M_SPORT_HUD

activ

PDC volume:

In PDC ECU:

default:

LAUTSTAERKE_HINTEN

e65

e60

RR1

e70

wert_06

changed last line to wert_02.

ASP_BEIKLAPPEN <- folding

ASP_BORDSTEIN <- passenger kerb function

ASP_EC_INPUT <- not sure what this does

ASP_LIN_SPIEGEL <-Tells the KGM to send mirror control codes over the LIN bus.

ASP_MEMORY <-mirror memory function

ASP_STANDHEIZUNG <- not sure, translation is stand heating

BEIKLAPPEN_B_KOMFORTSCHL <-mirror comfort folding

-in CAS module:

KOMFORT_EJECT -> aktiv

Basically, when shutting down hold the start/stop button and it should also eject the key fob out and in combination w/ ER_KEYOUT_AUTOVR it'll unlock the door(s) too.

MA testing (pre-LCI):

VERHALTEN_DRL_TFL_33 drl_s (angel eyes as DRL. This works with the entry below but they are much dimmer than the LCI. Probably won't be able to see them during the day)

DRL_TFL_SML_33 aktiv (angel eys as DRL)

DRL_TFL_TFL_33 (seems to do same thing as _SML_ )

DRL_TFL_RL_BL_1_33 (Tail lights on with DRL. Much too bright I think. )

aktiv

DRL_TFL_RL_BL_2_33 (Didn't notice anthing different)

aktiv

DRL_TFL_BLK_V_GED (Didn't notice anthing different)

nicht_aktiv

neither of these seemed to have any effect

TAGFAHRLICHT_ECE_2 DAYTIME RUNNING LIGHTS (EUROPE) 2

aktiv

TAGFAHRLICHT_ECE_3 DAYTIME RUNNING LIGHTS (EUROPE) 3

aktiv

ABSCHALTMELDUNG (power) - didn't test this

aktiv active

* nicht_aktiv not active

ABSTAND_KOPPLUNG (pitch generation) - no change

* aktiv active

nicht_aktiv not active

AKUSTIK_RECHTS_LINKS (Right and Left tones) - didn't test

* aktiv active

nicht_aktiv not active

AKUSTISCHE_FEHLERMELDUNG (acoustic error message) - didn't test

aktiv active

* nicht_aktiv not active

DYNAMIC_ABSCHALTEN_VORN (*DYNAMIC POWER OFF FORWARD) - no change

aktiv active

* nicht_aktiv not active

EINSCHALTMELDUNG_BEI_1MAL (power on 1 time?) - didn't test

aktiv active

* nicht_aktiv not active

EINSCHALTMELDUNG_IMMER (*power always) - no change

aktiv active

* nicht_aktiv not active

EINSCHALTVERZOEGERUNG (POWER ON DELAY) - didn't test

* aktiv active

nicht_aktiv not active

EIS_AUSBLENDEN (ice removing?) - didn't test

* aktiv active

nicht_aktiv not active

MELDUNG_TASTER (Release Button) -makes a tone when PDC button pressed

aktiv active

* nicht_aktiv not active

NOTFUNKTION (Emergency operation) - didn't test

aktiv active

* nicht_aktiv not active

NUR_KL15_BETRIEB (KL 15 OPERATION ONLY) - didn't test

* aktiv active

nicht_aktiv not active

PDC_AKTIV/DEAKTIV

rueckwaertsgang -Comes on in reverse gear and goes off when leave reverse

* weg_geschw (off speed?) - default behavior where PDC turns itself at specific speed

PDC_SCHALTER (*PDC switch or switches ?) - no change

aktiv active

* nicht_aktiv not active

STILLSTANDSMANAGEMENT (shutdown or turnaround management) - no change

aktiv active

* nicht_aktiv not active

TONGEBER (sounder)

aktiv active - disabled and caused check control

* nicht_aktiv not active

TONGEBER_HINTEN (Rear Sounder) - didn't test

gong

* lautsprecher loudspeaker

TONGEBER_VORN (Front or forward sounder) - no change

gong

* lautsprecher loudspeaker

SP_BEIKLAPPEN in the KGM module, I have to make it aktiv

To keep LCI (maybe pre-lci also??) AE's stay bright:

Go into LMA and look for:

PWM_AN_SL_V_AL_1_34

wert_06 - ** Change to wert_01 **

LMA

SIDEMARKER_US

nicht_aktiv

ain sensor sunroof/tilt closes when it rains

MSHD

REGENSCHLIESSEN

aktiv

REGENSCHLIESSENTILT

aktiv

this option worked for me.

BLINKIMPULS_WARNBLK to wert_02 using nettodat coding only makes it blink faster.

Autoheadlamp senstitivity

FLC_SCHWELLWERT_SATZ

wert_01

wert_02

wert_03

wert_04

REVERSE_GONG in CGATE and CAPPL enables the gong sound when the car is in reverse gear.

For module MSHD:

REGENSCHLIESSEN

activ

REGENSCHLIESSENTILT

activ

Flash to Pass, using the xenon instead of the halogen (default).

BI_XENON_BEI_LH akti

I got the sunroof rain-close to work.

cornering light part - AE's to stay bright when the headlights are on

PWM_AN_SL_V_AL_1_34 from wert_06 to wert_01

Break Force Display

Module : LMA

BFD_1_RL_BL_ERSCH_BILD = brake light

wert_03 = flashing

BFD_1_BL_M_ERSCH_BILD = 3 Brake light

wert_03 = flashing

BFD_1_RL_BL_1_ERSCH_BILD = brake light 1

wert_03 = flashing

BFD_1_RL_BL_2_ERSCH_BILD = brake light 2

wert_03 = flashing

BFD_1_NSL_ERSCH_BILD = rear fog lamp

wert_03 = flashing

Module: CAS

KOMFORTSCHLIESSUNG_FB (Close windows via key fob)

aktiv

Module: CAS

KOMFORT_EJECT (Hold start/stop button and it will eject keyfob)

aktiv

Module: CAS

HOME COMFORT (The ignition key must be touched only briefly to the ignition to start the car)

aktiv

Module: CIC (Fuel Stop suggestion in Route Guidance. Use Route Information to tell you at what point in your journey you will need to fill up based on current gass in your tank)

NAVI_FUELSTOP_PROPOSAL

Module: CIC (iDrive Display modes. Adds sub-menu with three options, Day Mode, Night Mode and Auto Mode)

NAVI_MAPMODE_AUTOMATIC

Module: ABG (CIC, Disables seat belt chime for passenger side)

SBR_BEIFAHRER_2_CD

Module: ABG (Disables seat belt chime for driver side)

SBR_FAHRER_1

WELCOME LIGHTS

WELCOME_LIGHT_ACTIVE	nicht_aktiv -> aktiv

DEF_WELCOMELIGHT_CKM	nicht_aktiv -> aktiv

UNP_WELCOMELIGHT_CKM	nicht_aktiv -> aktiv

WELCOMELIGHT_CKM_0	nicht_aktiv -> aktiv

WELCOMELIGHT_CKM_1	nicht_aktiv -> aktiv

WELCOMELIGHT_CKM_2	nicht_aktiv -> aktiv

WELCOMELIGHT_CKM_3	nicht_aktiv -> aktiv

(02) Module: CIC (Enable Settings Menu to save and change for options such as Language, Temperature, Speed etc).

EINHEITEN_MASTER

Hmi

(03) Module: CIC (Enable all eight buttons to be programmed on the CIC as apposed to six)

FBM_SELECTION

eight_buttons

(04) Module: CIC (Video in motion (Requires change to the CIC.C** file also)

Module: CIC

VIDEO_NUR_MIT_HANDBREMSE

nicht_aktiv

SPEEDLOCK_X_KMH_MAX_C0E

3_kmh

SPEEDLOCK_X_KMH_MIN_C0E

3_kmh

DEFAULT_DATUM

yyyy_mm_dd

DEFAULT_DRUCK_EINHEIT

psi

DEFAULT_SVS_DIALOG

standard

DEFAULT_TEMPERATUR

fahrenheit

DEFAULT_WEG_EINHEIT

km

DEFAULT_ZEIT_EINHEIT

12h

EINSTELLUNG_MEILEN

mls_us

RADIO_WEATHERBAND

aktiv

RADIO_COUNTRY

us

FM_BAND_KW

nicht_aktiv

FM_BAND_MW

aktiv

RADIO_AM_LW

aktiv

BAUART_CIC

limousine

AUDIO_SYSTEM_CIC

hifi

CHECK_IGNITIONC

aktiv

"VA_CORNERINGLIGHT" set to aktiv in the CAPPL

DRL_V_GEDIMMT function nicht_aktiv to turn off DRL on LM1.

SBR_BEIFAHRER_SGM (passenger)

nicht_aktiv

SBR_FAHRER_SGM (driver)

nicht_aktiv

pathway way lightning

HEIMLEUCHTEN_FUNKSCHL

aktiv

HEIMLEUCHTEN_KL58G

aktiv

DEF_HEIMLEUCHTEN_CKM

wert_02

HEIMLEUCHTEN_VERLAENG

nicht_aktiv

HEIMLEUCHTEN_ABBRUCH

nicht_aktiv

HEIMLEUCHTEN_SEND_OPT

wert_01

LMA:

HEIMLEUCHTEN_FUNKSCHL nicht_aktiv

aktiv

HEIMLEUCHTEN_VERLANG nicht_aktiv

aktiv

HEIMLEUCHTEN_ABRUSCH nicht_aktiv (Abort lights on trunkbutton)

aktiv

CAS:

SODERSTRAZTE_PAKINALARM nicht_aktiv

panikalarm

door gong while key is in ?

KOMBI:

CC_ZUENDSCHLUESSEL > aktiv

CAS:

VERRIEGELUNGSSCHWELLE Automatic locking doors speed wert_02 (5 km/h)

IHKA

ABWAHL_AC Keep AC off even when turning on the car (except when in AUTO mode) aktiv

UMLUFT_MEMORY Remember last ventilation speed aktiv

MIND_ANZ_ZYKL_TIPP_BLK Soft touch turn signal

cornering light

PWM_FL_NSW_FKT_ABBLIEGELI In AUTO mode, fog lights turn on on slow curves and on turn signal wert_02

DRL_V_GEDIMMT

wert_01 (us-drl) _02 (40% high beam)

DRL_WERT_DIMMUNG

wert_01

DRL_V_GEDIMMT

wert_01 = turn signals as DRL

wert_02 = halogen inner beam as DRL

DRL_WERT_DIMMUNG

wert_01 = 26%

wert_02 = 40%

the steering wheel tightness when on sport mode:

GESCHWIN_WERTE_SPORT_KGM

STROMWERTE_SPORT_KGM