| Service Measure |  |
| --- | --- |
| Lights | B63 202 04 | March 23, 2004 |

This Service Information bulletin supersedes S.M.B63 202 04 dated March 9, 2004.

Changes to this revision are identified in blue text.

Subject

#### Automatic headlamp system does not switch off the lights

Complaint

The following complaints regarding the automatic headlamps have been advised:

1. 	The dipped headlights are late in switching off following programming of the vehicle with CIP 9.4 or a more recent version.

2. 	Dipped headlights switch on spontaneously, even in daylight..

Vehicles concerned: E60

Cause

Normal operation

Measure

There have been no significant modifications to the automatic headlamps system for E60 since the start of series production.

The following settings may be selected using the Car and Key Memory:

- Normal

- Sensitive

- Very sensitive

In the normal setting, the lights switch off about 1/2 an hour later than in the sensitive setting (in the morning), or on about the same period earlier in the evening.

The situation is reversed in the very sensitive position.  The lights switch off about half an hour earlier in the morning, and on about half an hour later in the evening.

The headlamps switch off after a delay of about 5 seconds after the vehicle exits from a tunnel.  This value is fixed, and is influenced very little by the sensitivity levels.

The system has built-in hysteresis to prevent constant switching on and off.  This means that the threshold value for switching on the lights is at a lower light value than the threshold value for switching off.

As a matter of principle, the sensitivity of the two sensors detecting the brightness of the ambient light cannot match that of the human eye.  As a result, conditions sometimes occur where the human eye recognizes relatively bright conditions, but the automatic headlamps remain illuminated.  Typically, this condition occurs when the sun is low on the horizon.

Entering a tunnel with very bright street lighting in the center of the roadway is also a critical situation.  Street lighting radiates a high proportion of infrared and so the headlamps switch on relatively late even though the driver feels that they should really have switched on sooner.