|  | SI B 51 07 04 Body Equipment | July 2004 Technical Service |
| --- | --- | --- |

SUBJECT
Squeaking Noise from Door Seals

MODEL
E60 - 5 Series

E83 - X3 SAV

SITUATION
Some customers may complain that they hear squeaking noises coming from the doorframe area while driving.

CAUSE
The movement between the mating surface of the flock covered (felt-like material) door seal and the outer roof panel produces a squeaking noise.

PROCEDURE

|  | Clean the mating surfaces of the door seal (flock covered area) on all four doors with BMW Silicone Remover and let dry. Then apply Carbaflo to the flock covering on all four door seals. No further treatment is necessary after this application (such as drying, polishing the roof, etc.). |
| --- | --- |

PARTS INFORMATION

| Part Number | Description | Quantity |
| --- | --- | --- |
| 83 23 0 309 627 | Carbaflo lubricant | 1 |
| 83 19 9 407 906 | BMW Silicone Remover | 1 |

WARRANTY
For information only.

[ Copyright © 2004 BMW of North America, LLC ]