Look, Mommy, no warning triangle!!!

Having a hard time uploading the pictures, but here's the scoop:

You need a pair of 50-ohm, 10 watt resistors (similar to the ones jiio found at the MB site) +/-$2.00 at Radio Shack.

Remove the license plate light housing as diagrammed above. 

Remove the stock light

It is a tight fit, but bend the wire at each end of the resistor so it will slide through the holes in the contacts for the bulbs. Then place the resistor inside the housing, tucked against the edge, leaving room to place the LED festoon in the housing.

Place the LED festoon into the housing (make sure the LEDs are pointed in the right direction). There is plenty of room to fit the LED into the housing, as it shares the contacts with the resistor wires.

Both sides took a total of 5 minutes to complete. Turned the car on, lights on, no warning triangle. 

I know, I know, this post is worthless without pics, but I thought the info was worth it. It looks pretty sweet. I'll post pics when I figure it out...

PEACE

thank you bigguns and everyone else.. i got the resistors a t radio shack for $1.95 for 2 ..installed them and woala! no more warning triangule or message anymore.. ..but but it was a bit tricky making the resitor sit in place tight since the trunk gets opened and shut frequently...just make sure the resitor wires are bend making good pressure