# BMW TIS - 54 13 070 Removing and installing/replacing both floating roofliners for glass slide/tilt sunroof

Installation: 
Tensioning springs 1 must rest correctly in recess of floating roofliner 2. 
Adjust gap A = 3 ± 0.2 mm from control rail 3 to floating roofliner 2. 
Make sure washer 4 is correctly positioned with turning lock. 
Replace microencapsulated screws 5 and insert with Loctite. 
Tightening torque 54 12 11AZ .

Performing function check: 
· Floating roofliner must be able to move in control rail in X-direction. 
· Floating roofliner is positioned on right and can be pressed towards left under spring tension. 
· Floating roofliner springs back towards right into initial position.

| 54 13 070 | Removing and installing/replacing both floating roofliners for glass slide/tilt sunroof |
| --- | --- |
|  | Necessary preliminary tasks: · Remove glass slide/tilt sunroof lid at front and rear Note: Front and rear floating roofliners can be removed separately from each other. Make sure that grease on the rails does not come into contact with the floating roofliner. |
|  | Release screw 1. Release clips 2 with rotary block. Remove fan plate 3. Installation: Do not tighten down screw 1, fan plate 3 should be able to move in Y-direction. |
|  | Front floating roofliner: Open floating headliner approx. halfway. Front rain channel must be situated between first and second screws. Release screws 1. Tightening torque 54 12 10AZ . Remove star shims. Installation: Replace microencapsulated screws and insert with Loctite. Make sure star shims are correctly positioned. Pull out floating roofliner 2 in direction of arrow. If necessary, press wind deflector downwards. Installation: Carefully raise floating roofliner mechanism. |
|  | Rear floating roofliner: Close roofliner completely but not in fan position. Release screws 1. Remove tensioning springs (left side only) and washers. |
|  | Slide floating roofliner 4 in direction of arrow 1 between outer body skin and roofliner. Slide floating roofliner 4 up to end of control rail 3. Raise floating roofliner 4 and remove over control rail 3 in direction of arrow 2. |